## Slide 1
London Underground
Preliminary Results from Hampstead Measurement Campaign
Franklin Wilkins Building
29th January 2016
www.environment-health.ac.uk

## Slide 2: Agenda
Background
Analysis results so far
  Mass
  Aethalometer
  Laboratory Measurements
    EC/OC
    Elemental analysis (ICP-MS)
  Personal Exposure
Planned outputs

## Slide 3: Background
Increasing number of small personal exposure monitors available to public and in use for screening by LU
Monitors calibrated for ambient environment which has substantially different PM size, density and chemical composition
Lead to misinterpretation of data
Previous measurements
  IOM report (2003)
  130-480 µgm-3
  90% Fe

## Slide 4: Aims and Outputs
Develop scaling factor for personal exposure PM measurements (TSI Sidepak)
Develop scaling factor for LU’s TSI Dusttrak
Improve understanding of response of micro Aethalometer on LU
Higher time resolution reference measurements for PM mass
High time resolution measurements of elemental composition (C, Fe)
Higher quality measurements of black carbon

## Slide 5: Size fraction and time resolution
Size fraction
  Needed to measure PM2.5 for comparison to personal exposure monitors
  Routine black carbon measurements made in PM2.5
  Advantageous to measure a coarser size fraction to provide
    Additional scaling factor for Dusttrak
    Information on size distribution of PM
    Only had TSP inlet available for aethalometer
  Measurements undertaken in PM2.5 and TSP
Time resolution for filter analysis
  Concentrations expected to be low overnight and high during the day
  Needed to be high enough to capture range in concentration
  Sample had to be long enough to be above limit of detection
  4 hour samples chosen as a compromise

## Slide 6: Project Outline – Plan A
Mass measurements
  Filters using Partisol 2025
Personal Monitors
  TSI Dusttrak
  TSI Sidepak
  Micro-Aethalometer
Black Carbon
  Magee 7 wave length Aethalometer
Elemental and organic carbon
  Filters using Partisol 2025
Elemental composition
  XACT 625 X-ray Fluorescence

## Slide 7: Project Outline – Plan B
Mass measurements
  Filters using Partisol 2025
Personal Monitors
  TSI Dusttrak
  TSI Sidepak
  Micro-Aethalometer
Black Carbon
  Magee 7 wave length Aethalometer
Elemental and organic carbon
  Filters using Partisol 2025
Elemental composition
  Filters using Partisol 2025

## Slide 8: Mass measurements

## Slide 12: Regression Analysis

## Slide 13: Aethalometer (7 wavelength)

## Slide 14: Seven wavelengths aethalometer

## Slide 15
Chart: Time

## Slide 16: Laboratory measurements

## Slide 17: Sunset ECOC instrument

## Slide 18: Thermogram
FID Signal

## Slide 19: Elemental analysis (ICP-MS)
What additional elements do we measure?

## Slide 20: PERSONAL EXPOSURE

## Slide 21: Microaeth (Black), Particle Number Counter, Sidepak (Pm2.5

## Slide 22: Monitoring

## Slide 23
Line | Start | End | Duration
Victoria | 2014-12-08 09:03 | 2014-12-08 10:40 | 97 minutes
Circle | 2014-12-10 10:47 | 2014-12-10 13:27 | 160 minutes
Northern | 2014-12-16 08:07 | 2014-12-16 12:13 | 246 minutes
Bakerloo | 2015-02-04 08:07 | 2015-02-04 10:03 | 116 minutes
Jubilee | 2015-02-17 09:40 | 2015-02-17 13:53 | 253 minutes
District | 2015-03-03 10:07 | 2015-03-03 13:28 | 201 minutes
Piccadilly | 2015-03-17 09:25 | 2015-03-17 12:50 | 205 minutes
Docklands Light Railway | 2015-04-01 10:17 | 2015-04-01 14:35 | 258 minutes
Metropolitan | 2015-04-09 08:15 | 2015-04-09 12:30 | 255 minutes
Central | 2015-04-22 09:56 | 2015-04-22 13:36 | 222 minutes
 |  | Total | 34 hours

## Slide 27: Spatial variation
Londonair.org.uk/Research/tube_pm25/